## Slide 1: Disposition to calculation of IRFP4468PbF
Redefining of MOSFET current
MOSFET power loss in max current
  Conduction loss
  Switching loss (Assumption)
  Temperature
    Thermal capacitor of heat sink
Max speed power loss
Nominal temperature
Max temperature

## Slide 2: MOSFET minimum rating
Current to the Motor |  | 
Sinus peak | 300 | A
Current RMS | 212,1320344 | A, RMS
MOSFET max rating |  | 
Drain current in two MOSFET combined, RMS | 150 | A,RMS
Drain current in one MOSFET, RMS | 75 | A, RMS
Peak current in MOSFET | 150 | A
Vbat | 52,8 | V
Vds max rating | 100 | V

## Slide 3: Conduction loss
Conduction loss |  | 
Tempurtur junction (Tj) | 100 | °C
Rds(on) faktor | 1,644 | 
Rds(on) Typ. | 2,00E-03 | Ω
Rds(on) | 3,29E-03 | Ω
Pcon,Loss | 18,497 | W
Drain current in one MOSFET, RMS | 75 | A, RMS

## Slide 4: Switching loss – Defining the on and off time
Based on assumptions
What is need to be defined?

## Slide 5: Switching loss – Defining the on and off time
Rise and fall time of Vds

## Slide 6: Switching loss – Defining the on and off time
The fall time of the Id current
Assuming that Cgs is the same for on and off time. And it is equeal to Ciss at 50V
Cgs | 2,00E-08 | F

## Slide 7: Switching loss – Defining the on and off time
The Vgs voltage that makes Id=150A and Vds=52V

## Slide 8: Switching loss – Finding the off loss
Fsw = 20kHz
I gate off | 1,15 | A
Vgs(Io) | 4,56 | V
Vg th | 2 | V
tfi | 4,452E-08 | s
Time total | 3,045E-07 | s
Poff loss | 24,12 | W

## Slide 9: Switching loss – Finding the on loss
I gate off | 0,85 | A
Vgs(Io) | 4,56 | V
Vg th | 2 | V
tri | 8,024E-08 | s
Time total | 3,10E-07 | s
Poff loss | 24,571 | W
Fsw = 20kHz

## Slide 10: Total loss in one MOSFET
Conduction loss |  | 
Tempurtur junction (Tj) | 100 | °C
Rds(on) faktor | 1,644 | 
Rds(on) Typ. | 2,00E-03 | Ω
Rds(on) | 3,29E-03 | Ω
Pcon,Loss | 18,497 | W
Switching loss |  | 
Switching frequence | 20000 | Hz
Total sw loss | 48,689 | W
Total Loss in one MOSFET |  | 
P loss, total | 67,186 | W

## Slide 11: Thermal capacitor of heat sink
Thermal capacitor |  | 
Area | 8,75E-04 | m^2
Length | 8,40E-02 | m
Volume | 7,35E-05 | m^3
Correction factor of the volume | 2 | 
Real volume | 3,68E-05 | m^3
Density | 2700 | Kg/m^3
Mass | 0,099225 | Kg
c alu | 900 | J/(°C*kg)
Thermal capacitor (Cs) | 89,3025 | J/°C

## Slide 12: Max current step – 5s
The 5 seconds is from other calculations
Tempurtur MOSFET |  | 
Ta | 25 | °C
Time for max power | 5 | s
number of MOSFET on heat sink (n) | 1 | 
Ts | 28,720 | °C
Tc | 44,844 | °C
Tj | 64,328 | °C

## Slide 13: Current in max speed
Only wind resistance acts as load
Area of air drag | 0,6 | m^2
dimension number (C) | 0,804 | 
Air density | 1,3 | kg/m^2
Max speed | 50 | km/t
Max speed | 13,89 | m/s
Air drag force | 60,49 | N
Torque on wheel | 8,45 | Nm
Gear ratio | 0,24 | 
Torque from motor | 2,03 | Nm
Torque phas peak current rario |  | 
Max torque | 38 | Nm
Max phas peak current | 300 | A peak
Kt | 0,12667 | Nm/A
Phase current |  | 
Peak | 16,01 | A peak
RMS current | 11,32 | A RMS

## Slide 14: Max speed power loss
Current from continuously max speed |  | 
From phase RMS | 11,321 | A RMS
Current in the two MOSFET | 8,005 | A RMS
Current in one MOSFET | 4,003 | A RMS
Conduction loss from continuously max speed |  | 
Pcon, max speed | 0,052682095 | W
Switching loss from continuously max speed |  | 
Because it is too difficult to calculate the Switching loss in max speed, it will be asumed that the loss is 5W |  | 
Psw, max speed | 5 | W
Total Loss in one MOSFET from max speed |  | 
P loss, total | 5,052682095 | W

## Slide 15: Nominal temperature
Norminal power loss in one MOSFET |  | 
Procent Time there is: |  | 
Max current | 33,33 | %
Max speed | 33,33 | %
Down accelaration | 33,34 | %
In down accelaration there is no power loss |  | 
The norminal power loss is therefore; | 24,07710456 | W
Tempurtur due to norminal power loss |  | 
Ts | 85,19276141 | °C
Tc | 90,9712665 | °C
Tj | 97,95362683 | °C

## Slide 16: Max temperature
Two system

## Slide 17: Max tempurtur
Tempurtur MOSFET delta |  | 
Delta power loss | 43,109 | W
Ts | 0,961 | °C
Tc | 11,307 | °C
Tj | 23,809 | °C
Tempurtur in one MOSFET |  | 
Ts | 86,154 | °C
Tc | 102,2785 | °C
Tj | 121,7624 | °C